## Slide 1: RADIOLOGIC
CUT YOUR CABLES – MINIMIZE YOUR COST

## Slide 2
RL-MB-Link
Modbus Link
Modbus RTU link
Wireless MODBUS RTU
network with up to 64 nodes, each node can handle a complete RTU network.
433 MHz Radio
1000 m range
RL-PRIO-MB
Master
10 inputs * Digital * 0-10v * 0-30v
PLC * 32 logic inputs * 32 logic output * 32 registers
RL-Router
433 MHz Radio
1000m range
Modbus TCP
LTE
TCP/IP
UDP/IP
DHCP
HTTP
RL-PRIO
433 MHz Radio
1000 m range
10 Digital out
10 inputs * Digital * 0-10v * 0-30v
PLC * 32 logic inputs * 32 logic output * 10 registers
RL-PROP
433 MHz Radio
1000 m range
8 analog out * 0-10v * 0-20mA * 4-20mA
10 inputs * Digital * 0-10v * 0-30v
PLC * 32 logic inputs * 32 logic output * 10 registers
RL-PROP44
433 MHz Radio
1000 m range
4 analog out * 0-10v * 0-20mA * 4-20mA
4 digital out
10 inputs * Digital * 0-10v * 0-30v
PLC * 32 logic inputs * 32 logic output * 10 registers
RL-PRIO-MB
Modbus RTU Slave
* 64 input * 64 output
433 MHz Radio
1000 m range
10 Digital out
433 MHz Radio
1000 m range
10 Digital out
Modbus RTU customizable master.
RL Modules

## Slide 3
RL-DISPLAY
433 MHz Radio
1000 m range
7” capacitive touch display
Fully customizable layout for optimal customer functionality.
Easy to program and customize in the LogicLink application.
PLC * 64 logic inputs * 64 logic output * 10 registers
Event based programming for both graphics, alarm and input/output.
RL-RC8-D4
433 MHz Radio
250 m range
4 output function buttons
3 layer function buttons
Display with up to 10 visible indicators (on/off)
Customizable indicator layout for optimal customer functionality
Easy to program and customize in the LogicLink application.
64 output
64 input
RL-RC10
433 MHz Radio
250 m range
10 dual output function buttons
3 indicator LEDs (Green/red/off)
Easy to program and customize in the LogicLink application.
20 output
6 input
RL Transmitters

## Slide 4
RL LogicLink
Advanced programing made simple!
Point-and-click configuration combined with an easy-to-use graphical design GUI editor and the intuitive PLC editor make programming quick and painless.

## Slide 5
RL-Router
Collect all data.
Send to cloud.
Recieve and transmitt information from cloud, remote manage or analyze
RL-PRIO
Sensordata
Input 0–10V
PLC
If UI01 active
Activate Q02
digital output
RL-PROP
Sensordata from PRIO
output 0–10V
on AQ01
PLC If data from PRIO bellow 3V, send alarm to…
RL-PRIO-MB
Master
Sensordata from MODBUS RTU
PLC If ALARM from RL-PROP
Read register RXXX If RXXX below 54 activate UQ0/1
If data from PRIO bellow 3V, show warning in field
If RXXX below 54 show urgent warning on display
Touch functions, transmitt and ask for acnolidgement
Present result on screen.
Usage example
RL-RC8
button functions, transmitt and
ask for acnolidgement
Present inputs on display

## Slide 6
RL PRIO, RL PRIO-MB, RL-MB-Link

## Slide 7
RL PROP

## Slide 8
RL ROUTER

## Slide 9
RL DISPLAY